## Slide 1: Strategies for Reuse of Launch Vehicle First Stages
Matthew Vernacchia
Kelly Mathesius
2018-10-03
Are any first stage reuse strategies economically worthwhile?
… under what mission, market, and technological conditions?

## Slide 2: Some launch providers are moving towards 1st stage reusability
Will providers of expendable launch vehicles be left behind?
… or are these development efforts wasting billions?
SpaceX
Falcon 9
Operational
Blue Origin
New Glenn
In development
ULA
Vulcan SMART reuse
In development
Boeing
XS-1 Phantom Express
In development
Intro | Methods | Results | Conclusion
Image credits: Space Exploration Technologies, Blue Origin, United Launch Alliance, and The Boeing Company

## Slide 3: Many first stage reuse strategies have been proposed …
Launch site recovery
Downrange recovery
Falcon 9
USAF RBS
Baikal
Falcon 9
New Glenn
Ares I
XS-1 Phantom Express
Vulcan SMART
Examples:
… but their performance and cost have not been (publically) compared under a common framework
… and there remains controversy as to which, if any, are economically worthwhile
Intro | Methods | Results | Conclusion

## Slide 4: Cost per flight is estimated with performance and cost models
Estimate vehicle size
Estimate operations and refurbishment costs
Estimate 1st stage production cost
Estimate 2nd stage production cost
Estimate cost per flight
Estimate 1st stage production amortization share
masses
mission orbit
strategy
payload size
Performance Model
Cost Model
Cost per flight
+uncertainty (Monte Carlo)
+uncertainty (Monte Carlo)
Intro | Methods | Results | Conclusion

## Slide 5: Payload capacity is set by and inert mass
Tsiolkovsky
Specific impulse
Inert mass fraction
Payload mass fraction
Technology limits achievable specific impulse and inert mass fraction
Based on modern
kerosene/O2 stages
Intro | Methods | Results | Conclusion

## Slide 6: Reuse adds mass to the first stage, decreasing payload capacity
Recovery hardware
Recovery propellant
“unavailable” mass fraction
expendable inert mass fraction
Payload mass fraction
For each reuse strategy:
Recovery hardware distribution fit to detailed studies
Recovery propellant calculated fro maneuvers with dispersed parameters
Model output: element masses to cost model
Intro | Methods | Results | Conclusion

## Slide 7: TRANSCOST model relates masses to costs
Cost Estimating Relationships (CERs):
, – empirically fit point parameters based on historical data
Stage production costs are the sum of elements’ production costs:
Intro | Methods | Results | Conclusion

## Slide 8: Quantifying uncertainty for TRANSCOST parameters
digitize TRANSCOST historical data
regress data, establish confidence bounds for ,
Cost estimating relationship:
, drawn from triangular distribution bounded by 95% confidence interval of regressed data
Intro | Methods | Results | Conclusion

## Slide 9: Cost model estimates are credible
Intro | Methods | Results | Conclusion

## Slide 10: Downrange propulsive landing has lowest estimated cost
Lowest estimated cost
Intro | Methods | Results | Conclusion

## Slide 11: Cost decreases with number of reuses … up to a point
Confidently cheaper than expendable:
> ~5 uses
Realize most of cost savings:
> ~20 uses
Cost increases due to refurbishment:
> ~60 uses
LEO mission, 10 Mg payload
stage 1&2: kerosene gas gen. tech.
5
20
60
Intro | Methods | Results | Conclusion

## Slide 12: Reuse is more worthwhile for medium to heavy launch vehicles
Medium 10 Mg payload
Small 100 kg payload
LEO mission
stage 1&2: kerosene gas gen. tech.
Intro | Methods | Results | Conclusion

## Slide 13: Future work: development costs
This work only addressed recurring costs (cost-per-flight)
But development costs are also significant
Area for further study
Hypothesis: high launch rates are needed to justify developing reusability
Intro | Methods | Results | Conclusion

## Slide 14: Conclusion: Some 1st stage reuse strategies, particularly downrange propulsive landing, can reduce cost per flight
Downrange propulsive landing is likely the lowest-cost strategy
  Partial (engines-only) reuse strategies have small potential savings
  Winged stages have uncertain (and probably high) production costs
Only worthwhile for medium-large launch vehicles, where first stage production costs dominate
Intro | Methods | Results | Conclusion

## Slide 15: Questions?
Launch site recovery
Downrange recovery
Falcon 9
USAF RBS
Baikal
Falcon 9
New Glenn
Ares I
XS-1 Phantom Express
Vulcan SMART
Examples:

## Slide 16
Backup Slides

## Slide 17: All reuse strategies reduce the payload mass fraction
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion