## Slide 1: Strategies for Reuse of Launch Vehicle First Stages
Matthew Vernacchia
Kelly Mathesius
2018-10-03
Are any first stage reuse strategies economically worthwhile?
… under what mission, market, and technological conditions?

## Slide 2: Some launch providers are moving towards reusability
Will providers of expendable launch vehicles be left behind?
… or are these development efforts wasting billions?
SpaceX
Falcon 9
Operational
Blue Origin
New Glenn
In development
ULA
Vulcan SMART reuse
In development
Boeing
XS-1 Phantom Express
In development
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion

## Slide 3: Many first stage reuse strategies have been proposed …
Launch site recovery
Downrange recovery
Falcon 9
USAF RBS
Baikal
Falcon 9
New Glenn
Ares I
XS-1 Phantom Express
Vulcan SMART
Examples:
… but their performance and cost have not been (publically) compared under a common framework
… and there remains controversy as to which, if any, are economically worthwhile
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion

## Slide 4: Cost per flight is estimated with performance and cost models
Estimate vehicle size
Estimate operations and refurbishment costs
Estimate 1st stage production cost
Estimate 2nd stage production cost
Estimate cost per flight
Estimate 1st stage production amortization share
masses
mission orbit
strategy
payload size
Performance Model
Cost Model
Cost per flight
+uncertainty (Monte Carlo)
+uncertainty (Monte Carlo)

## Slide 5: TRANSCOST model relates masses to costs
Cost Estimating Relationships (CERs):
, – empirically fit point parameters based on historical data
Stage production costs are the sum of elements’ production costs:

## Slide 6: Quantifying uncertainty for TRANSCOST parameters
digitize TRANSCOST historical data
regress data, establish confidence bounds for ,
Cost estimating relationship:
, drawn from triangular distribution bounded by 95% confidence interval of regressed data

## Slide 7: First stage reuse can be economically worthwhile
First stage production cost drives the high cost per flight of expendable vehicles (for large vehicles)
Downrange propulsive landing is likely the lowest-cost strategy
1st stage reuse is worthwhile only for large payloads and high launch rates
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion

## Slide 8: Cost model estimates are credible
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion

## Slide 9: First stage production cost drives cost per flight
reuse
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion
Expendable
With first stage reuse
LEO mission, 10 Mg payload
stage 1&2: kerosene gas gen. tech.

## Slide 10: Different reuse strategies result in different vehicle masses and costs
Reuse:
Adds mass to the first stage
Reduces the payload mass fraction
Estimate element masses
Estimate cost
Payload mass fraction
=
Estimate payload mass fraction
Recovery hardware
Recovery propellant
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion

## Slide 11: All reuse strategies reduce the payload mass fraction
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion

## Slide 12: Downrange propulsive landing has lowest estimated cost
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion
Lowest estimated cost

## Slide 13: Cost decreases with number of reuses … up to a point
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion
Confidently cheaper than expendable:
> ~5 uses
Realize most of cost savings:
> ~20 uses
Cost increases due to refurbishment:
> ~60 uses
LEO mission, 10 Mg payload
stage 1&2: kerosene gas gen. tech.
5
20
60

## Slide 14: Reuse is only viable for medium to heavy launch vehicles
Medium 10 Mg payload
Small 100 kg payload
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion
LEO mission
stage 1&2: kerosene gas gen. tech.

## Slide 15: High launch rates enable reuse development to be paid off
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion

## Slide 16: Conclusion: Some 1st stage reuse strategies, particularly downrange propulsive landing, can be economically worthwhile
Downrange propulsive landing is likely the lowest-cost strategy
  Partial (engines-only) reuse strategies have small potential savings
  Winged stages have uncertain (and probably high) production costs
Only worthwhile for medium-large launch vehicles, where first stage production costs dominate
High launch rates (> 20/year) are likely needed to pay off development costs
Intro | 1. Production costs | 2. Lowest-cost strategy | 3. Conditions for reuse viability | Conclusion